## Slide 1: Namhun, Kim (Bachelor’s Course) System Semiconductor Engineering University of Sangmyung
Summer 2022
Final Product Description

## Slide 2: Contents
Idea
  Module & Testbench format
  Pseudo Code
Structure
  Function Structure
Implementation

## Slide 3: Idea
Module & Testbench format
module buffer_4bit (clk, in, out);
input [3:0] in;
input clk;
output reg [3:0] output;
always @(posedge clk) begin
output <= in;
end
endmodule
module testbench();
reg [3:0] in;
reg clk;
wire [3:0] output;
buffer_4bit test_unit(clk, in, out);
initial clk = 1’b0;
always #1 clk = ~clk;
initial begin
in = 4’b1010; @(negedge clk);
in = 4’b1111; @(negedge clk);
$stop;
end
endmodule

## Slide 4: Idea
Module & Testbench format
module buffer_4bit (clk, in, out);
input [3:0] in;
input clk;
output reg [3:0] output;
always @(posedge clk) begin
output <= in;
end
endmodule
module testbench();
reg [3:0] in;
reg clk;
wire [3:0] output;
buffer_4bit test_unit(clk, in, out);
initial clk = 1’b0;
always #1 clk = ~clk;
initial begin
in = 4’b1010; @(negedge clk); in = 4’b1111; @(negedge clk);
$stop;
end
endmodule

## Slide 5: Idea
Module & Testbench format
module buffer_4bit (clk, in, out);
input [3:0] in;
input clk;
output reg [3:0] output;
always @(posedge clk) begin
output <= in;
end
endmodule
module testbench();
reg [3:0] in;
reg clk;
wire [3:0] output;
buffer_4bit test_unit(clk, in, out);
initial clk = 1’b0;
always #1 clk = ~clk;
initial begin
in = 4’b1010; @(negedge clk);
in = 4’b1111; @(negedge clk);
$stop;
end
endmodule

## Slide 6: Idea
Module & Testbench format
module buffer_4bit (clk, in, out);
input [3:0] in;
input clk;
output reg [3:0] output;
always @(posedge clk) begin
output <= in;
end
endmodule
module testbench();
reg [3:0] in;
reg clk;
wire [3:0] output;
buffer_4bit test_unit(clk, in, out);
initial clk = 1’b0;
always #1 clk = ~clk;
initial begin
in = 4’b1010; @(negedge clk);
in = 4’b1111; @(negedge clk);
$stop;
end
endmodule

## Slide 7: Pseudo Code
Replace keyword input/output/output reg to reg/wire
(Example)
input in;  reg in;
output out;  wire out;
2. Create Module Instance String
(Example)
  module not(in, out);  not not(in, out);  not test_unit(in, out);
3. If “Clock” Exist, Create clk/rst State
4. Create TestVector via Wavedrom JSON
5. Write “testbench.v”

## Slide 8: Structure
Functions
__main__
tb_gen
get_module_name
wave_interpreter
print_err
file_test
get_io
module_instance
tv_gen

## Slide 9: Structure
__main__

## Slide 10: Structure
tb_gen()
“testbench.v”
`timescale 1ns/1ns
module testbench();
inout
instance
(clk/rst)  Optional
testvector
endmodule

## Slide 11: Structure
tb_gen()
Testbench Contents List
Write “testbench.v”

## Slide 12: Structure
file_test() & print_err()
Check File Extension.
Example)
*name = [“test.txt”, ”test.v”]
ext1 = “test.txt”  [“test”, “txt”][-1] == “txt”
ext2 = “test.v”  [“test”, “v”][-1] == “v”
Print Error Message with Highlight.
Example)

## Slide 13: Structure
get_io()
Redefine module data,
Replace input  reg
Replace output reg  wire
Replace output  wire
Return Testbench formatted I/O State

## Slide 14: Structure
get_module_name()
Module Name Extraction
(In Function Processing)
name = “module and_gate(in, out);”
name = [“module”, “and_gate(in,” , “out)”]
name = name[1] == “and_gate(in,”
#name.split(“(“)[0].strip() == “and_gate“
(In “module.v”)
module and_gate(in, out);\n
input in;\n
output out;\n
...
endmodule

## Slide 15: Structure
module_instance()
(Example)
  module not(in, out);  not not(in, out);  not test_unit(in, out);

## Slide 16: Structure
tv_gen()
Declare Variables
Open & Check Json file

## Slide 17: Structure
tv_gen()
Get Input Signals from json
“example.json”
{signal:[
{name:"a", wave:"l...h..."},
{name:"b", wave:"l.h.l.h."},
{name:"c", wave:"lhlhlhlh"},
{},
{name:"out", wave:"l......h"}
]
}
input
output

## Slide 18: Structure
tv_gen()
Create Testvector
“example1.json”
{signal:[
{name:"clk", wave:"P......."},
{name:"rst", wave:"lh......"},
{name:"d", wave:"hlhlhlhl"},
{},
{name:"out", wave:"l.hlhlhl"}
]
}
“example2.json”
{signal:[
{name:"a", wave:"l.h."},
{name:"b", wave:"lhlh"},
{},
{name:"out", wave:"l..h"}
]
}

## Slide 19: Structure
tv_gen()
Set Sim Stop time
initial verilog_clk = 1’b1;
always #1 verilog_clk = ~clk;
{name:”json_clk”, wave:”P...”}

## Slide 20: Structure
wave_interpreter()
“example1.json”
{signal:[
{name:"clk", wave:"P......."},
{name:"rst", wave:"lh......"},
{name:"d", wave:"hlhlhlhl"},
{},
{name:"out", wave:"l.hlhlhl"}
]
}
“example2.json”
{signal:[
{name:"a", wave:"l.h."},
{name:"b", wave:"lhlh"},
{},
{name:"out", wave:"l..h"}
]
}

## Slide 21: Structure
wave_interpreter()
“example.json”
{signal:[
{name:"a", wave:"hl.."},
{name:"b", wave:"lhl."},
{name:"c", wave:"l.hl"},
{name:"d", wave:"l..h"},
{},
{name:"out",wave:"====",
data:["00","01","10","11"]}
]
}

## Slide 22: Structure
wave_interpreter()
“example.json”
{signal:[
{name:"clk", wave:"P."},
{name:"rst", wave:"h."},
{name:"in",wave:"==",
data:["0000","1111"]},
{},
{name:"out", wave:"==",
data:["0000", "1111"]}
]
}

## Slide 23: Implementation
Error Case
Operating System: Ubuntu 20.04.4 LTS
Working Directory: /home/skagns/tbgen
Python Version: 3.8.10
File Test Failed
Args Seq Error
Json File Error

## Slide 24: Implementation
Sequential Logic Test (Binary Counter)
Operating System: Ubuntu 20.04.4 LTS
Working Directory: /home/skagns/tbgen
Python Version: 3.8.10
binary counter module
binary counter wavedrom

## Slide 25: Implementation
Sequential Logic Test (Binary Counter)
Operating System: Ubuntu 20.04.4 LTS
Working Directory: /home/skagns/tbgen
Python Version: 3.8.10

## Slide 26: Implementation
Non-Clock-Dependent Logic Test (halfadder_4bit)
Operating System: Ubuntu 20.04.4 LTS
Working Directory: /home/skagns/tbgen
Python Version: 3.8.10
wavedrom json
module

## Slide 27: Implementation
Non-Clock-Dependent Logic Test (halfadder_4bit)
Operating System: Ubuntu 20.04.4 LTS
Working Directory: /home/skagns/tbgen
Python Version: 3.8.10