## Slide 1: Namhun Kim (Bachelor’s course) System Semiconductor Engineering University of Sangmyung
Summer Bootcamp 2022
Verilog HDL: Chapter 1 ~ 3

## Slide 2: Contents
Learning Object
  1. Understanding Verilog
  2. *.v files simulation
  3. Fundamental Language Structure of Verilog

## Slide 3: Verilog HDL?
About Verilog HDL
  Verilog HDL = Verilog Hardware Description Language
“Similarly, in the digital design field, designers felt the need for a standard
language to describe digital circuits. Thus, HDLs came into existence.”
-Verilog HDL: A Guide to Digital design and Synthesis-

## Slide 4: Verilog HDL?
About Verilog HDL
  Verilog HDL = Verilog Hardware Description Language
  Verilog HDL != VHDL(VHSIC HDL)
“Similarly, in the digital design field, designers felt the need for a standard
language to describe digital circuits. Thus, HDLs came into existence.”
-Verilog HDL: A Guide to Digital design and Synthesis-

## Slide 5: Digital Design Process
Design Specification
Behavioral Description
RTL Description(HDL)
Verification & Test
Gate-Level Netlist
Physical Layout
Implementation

## Slide 6: Digital Design Process
Design Specification
Behavioral Description
RTL Description(HDL)
Verification & Test
Gate-Level Netlist
Physical Layout
Implementation
Behavioral Description
RTL Description(HDL)
Verification & Test
We Handle This!

## Slide 7: Configuration of Verification & Test
Verification & Test
  1. Functional Verification
    Check whether hardware’s function is working perfectly
      Testbench is used to Check functionality
  2. Logic Synthesis/ Timing Verification
    Check the RTL level Issues
      Timing Diagram Check using Testbench
RTL: Registor Transfer Level
Registor: a collection of FF
Resistor: 저항
Registor: 레지스터

## Slide 8: Installation ModelSim
My Github: https://github.com/namu00/2022-Summer/tree/main/Verilog_Study
  Download and Flow the guide.docx

## Slide 9: Blah~ Blah~
Blah~
  Blha~

## Slide 10: Blah~ Blah~
Blah~
  Blha~
개발 폰트는 Naver D2Coding 또는 Consolas를 추천합니다.
00 oO iI ll //맑은고딕
00 oO iI lL //Consolas
00 oO iI lL //D2 Coding

## Slide 11: Module & Module Instance
Module
  4bit full adder
module fulladd4(sum, c_out, a, b, c_in);
output [3:0] sum; // 4비트 배열 선언
output c_out;
input [3:0] a; // 4비트 배열 선언
input [3:0] b; // 4비트 배열 선언
input c_in;
assign {c_out, sum} = {1’b0, a} + {1’b0, b}
endmodule
module <MODULE_NAME> (TERMINAL_LIST);
...
//Module Internals
...
endmodule

## Slide 12: Module & Module Instance
Module Instance
  In 16bit full adder code..
module fulladd16(sum, c_out, a, b, c_in)
...
fulladd4 unit_0( .a(a[3:0]),
.b(b[3:0]),
.sum(sum[3:0]),
.c_in(c_in),
.c_out(c_out_0));
fulladd4 unit_1(sum[7:4], c_out_1, a[7:4], b[7:4], c_out_0);
fulladd4 unit_2(...);
fulladd4 unit_3(...);
...
endmodule

## Slide 13: Module & Module Instance
Module Instance
  In 16bit full adder code..
module fulladd16(sum, c_out, a, b, c_in)
...
fulladd4 unit_0( .a(a[3:0]),
.b(b[3:0]),
.sum(sum[3:0]),
.c_in(c_in),
.c_out(c_out_0));
fulladd4 unit_1(sum[7:4], c_out_1, a[7:4], b[7:4], c_out_0);
fulladd4 unit_2(...);
fulladd4 unit_3(...);
...
endmodule
Module Instance Declaration!

## Slide 14: Module & Module Instance
Module Instance
  Module Instance Declaration Form
module <MODULE_NAME> (TERMINAL_LIST)
...
<MODULE> <INSTANCE_NAME_0> (TERMINAL_LIST);
<MODULE> <INSTANCE_NAME_1> (TERMINAL_LIST);
...
endmodule

## Slide 15: Hierarchy Concept
Top-Down
16 Bit Full Adder
Unit_0
Unit_1
Unit_2
Unit_3
Logic Gates
Logic Gates
Logic Gates
Logic Gates

## Slide 16: Hierarchy Concept
Bottom-Up
16 Bit Full Adder
Unit_0
Unit_1
Unit_2
Unit_3
Logic Gates
Logic Gates
Logic Gates
Logic Gates

## Slide 17: StimulusBlock & Testbench
Stimulus Block Concept
(Stimulus Block)
16Bit Full Adder
a
b
carry_in
sum
carry_out

## Slide 18: StimulusBlock & Testbench
Stimulus Block Concept
Stimulus
Block
(Top Level Block)
a
b
c_in
c_out
sum
Design Block
16bit
F_add
a
b
c_in
c_out
sum

## Slide 19: Blah~ Blah~
Blah~
  Blha~

## Slide 20: Language Structure
Comments
Operators
// One line comment
/* multiple line comment */
// Similar like C language
a = a + b; // 합
a = a – b; // 차
a = ~b; // 논리 부정
a = b && c; // AND연산
a = b || c; // OR연산
a = b ? c : d; // 조건 연산
//...etc

## Slide 21: Language Structure
Numbers
String
4’b1111 // 4비트 2진수 1111
12’habc // 12비트 16진수 abc
16’d255 // 16비트 10진수 255
1234 // 10진수 1234, 형식을 지정하지 않은 숫자는 기본적으로 10진수 취급
4’bx // 4비트 미지수 x
8‘dz // 8비트 하이-임피던스
“Hello, World!” // 문자열 표현

## Slide 22: Language Structure
Key-words
  reg == input signal
  wire == output signal
Key-word | Definition
reg | 일반적으로 사용하는 레지스터
wire | 디바이스의 물리적인 연결, 값 저장 x
real | 실수 표현 레지스터
time | 시간 저장 레지스터
integer | 정수 표현 레지스터 (signed형태 사용 가능)

## Slide 23: Language Structure
input / output
  input == input
  output == output
module not_gate(in, out);
input in;
output out;
assign s = ~in;
endmodule
module half_adder(a, b, sum);
input a;
input b;
output sum;
assign sum = a + b;
endmodule

## Slide 24: Language Structure
Key-word example
module half_adder(a, b, sum);
input a;
input b;
output sum;
assign sum = a + b;
endmodule
half_adder.v
testbench.v
module testbench();
reg a;
reg b;
wire sum;
half_adder ha (a, b, sum);
initial begin
#10 a = 1'b0; b = 1'b0;
#10 a = 1'b0; b = 1'b1;
#10 a = 1'b1; b = 1'b0;
#10 a = 1'b1; b = 1'b1;
#10 $stop;
end
endmodule

## Slide 25: System Task
Task | Definition
$display | Shell에 값을 출력
$time | 시간을 보여줌
$stop | 작업을 중단함
$finish | 작업을 그만 둠
module testbench();
reg a;
reg b;
wire sum;
half_adder ha (a, b, sum);
initial begin
#10 a = 1'b0; b = 1’b0;
$display("%t ns : a = %d, b = %d", $time, a, b);
#10 a = 1'b0; b = 1’b1;
$display("%t ns : a = %d, b = %d", $time, a, b);
#10 a = 1'b1; b = 1’b0;
$display("%t ns : a = %d, b = %d", $time, a, b);
#10 a = 1'b1; b = 1’b1;
$display("%t ns : a = %d, b = %d", $time, a, b);
#10 $stop;
end
endmodule

## Slide 26: Extension
Linux Shell command
  cd : Change Directory
  ls : list
    ★ls –l★

## Slide 27: Extension
Linux Shell command
  clear : Clear Screen